Service Level

Ryobi Technologies, Inc.

Anderson, SC.

SERVICE INFORMATION

Product – BS1001SV Ryobi 10 in. Band Saw with Silent Vac Dust Collection System

Condition – If the product is brought in for service with a complaint of excessive up and down movement of the table, the table trunnion bolt will need to be replaced.

Affected Products – BS1001SV Band Saws with a manufacture date code between 0414 and 0432, require the replacement of the table trunnion bolt.

Service Procedures – Tighten the table bevel lock knob. Using a 10mm socket or end wrench, remove the original table trunnion bolt and replace with the new bolt. Tighten the trunnion bolt until the inner derlin (plastic) washer is snug against the trunnion. Loosen the bevel lock knob, rotate the bevel adjust knob to change the angle of the table tilt. When the trunnion bolt is tight enough there should be minimal resistance felt when the table is tilted.

Service Components Required

1 ea. Table Trunnion Bolt ---------------------------------pt. #028977000

Submit warranty claim using warranty code -------- BS1001SB1

Warranty claim compensation -------------------------------- $20.00

For technical assistance contact Ryobi technical support at 1-800-525- 2579

# Text boxes

MANDATORY