Service Level

RYOBI Technologies, Inc.

SERVICE BULLETIN

Product – CSB140LZ

Identification – Ryobi 7 1/4” Circular Saw, with Laser Guide

Condition – The laser battery cover will not stay in place or is missing from the product.

Remedy – Replace the laser guide housing and cover as an assembly.

Service Components Required

1 ea. -------------------------------- 200314001 Laser Guide Housing Assembly

Service Procedures

- Unplug the saw from the power source.

- Make sure the laser is turned off.

- Remove the laser cover by squeezing the two front corners and lift it off the base. Fig. #1

- Remove the two AAA laser batteries.

- Remove the Laser Guide retaining screw on the back of the laser housing. Fig. #2

- Lightly squeeze the front of the lower housing and lift the base from the upper guard. Fig. #3.

- Using needle nose pliers, carefully disconnect the battery and laser wires from the switch. Fig. #4

- Using a small blade screwdriver release the spring loaded tabs holding the                      switch from bottom housing. Fig. #5

- Carefully lift off the switch.

- Re-install the switch into the new housing with the “O” facing the front of the saw.

  - Note: push the rubber boot down from the top of the switch to ensure that the boot protects the rocker switch on all four sides. Fig. #6

  - Make sure that the switch lock tabs release locking the switch to the bottom housing locking the switch in place. Fig. #5

- Re-attach the wire from the laser to the switch terminal towards the front “O” of the housing. Fig. #4

- Re-attach the wire from the batteries to the switch terminal towards the rear “I” switch terminal.

- Rout the wires from the switch into the cut-out in the top of the guard while re-installing the lower laser guide housing. Fig. #7

  - Inspect the wires to ensure that no wires are pinched between the housing and the upper guard.

- Align the tabs on the bottom front of the laser guide housing with the upper guard and snap into place.

- Install the retaining screw on the rear of the housing and tighten. Fig. 2

- Align the “+” and “-“ terminal locations of the battery to match the inside of the battery housing. Snap the batteries in place.

- Install the new laser cover.

- Test the operation of the laser.

For technical assistance contact Ryobi technical support at

1-800-525-2579

# Text boxes

MANDATORY